## Slide 1
Hindustan Aeronautics Limited
Network
Administrator
Users
Single Sign-On*
ID Management
Red Hat OpenShift Cluster
Customer Locations -
HAL Network
Porbandar,
GJ
Ratnagiri,
MH
Chennai,
TN
Bhuvaneshwar,
OD
Sri Vijaya Puram, Andaman and Nicobar Islands
Kochi,
KL
Sterling File Gateway
Control Center
Monitor / Director
Flight Data Recorder
UI Services
MAS Core
UI Services
MAS Applications
Maximo Application Suite
Application API Services
Administration services
User Management
Workspace Management
Shared License service
Relational Database
Maximo Manage – Asset Data
Maximo Monitor – Config Data
Maximo Health – Sensor Data
Maximo Predict – Analytics Data
Cloud Object Store
Maximo Visual Inspection – Images
Analytics – Results Data
IFS Application
REST API
AI Model- Project Data
Red Hat OpenShift - Configuration
SevOne
Data Insight
vPAS NMS
vPAS NMS
vDNC
Instana
IoT Tool – Historical Data
Add-on Applications
Document Database
MAS Core – Services Configuration
IoT Tool - Configuration
Visual Inspection - Configuration
Persistent Volumes
Analytics Services
Watson Studio
Watson Discovery
Asset Configuration Manager
Scheduler Optimization
Maximo Mobile Anywhere
Poll
NetFlow, sFlow, etc.
Config / Performance
Config / Performance
Config / Performance
Stream Processor
Instana Agent
Communication
Sensors
Traces
Data Stores
UI Backend
HAL Integrated Asset Management & Monitoring Platform Solution Architecture
Secure File Gateway
Devices
API Key
Connection / Messaging Services
Proxy Service, Message Gateway
Device & Security Management
Apache Kafka
Maximo® Application Suite
Reporting & Allied Software

## Slide 2
Red Hat OpenShift Cluster
Metrics & Logs
Instana
Stream Processor
Instana Sensors enabled in Agents on Worker Nodes
Data Stores
UI Backend
HAL Integrated Observability Solution
Maximo® Application Suite
IT Head/Infra Head
Single Sign-On*
ID Management
Tickets
Metrics & logs
Hindustan Aeronautics Limited
Network
Interfaces

## Slide 3
IT Head/Infra Head
Netops Team
Single Sign-On*
ID Management
Customer Locations -
HAL Network
Porbandar,
GJ
Ratnagiri,
MH
Chennai,
TN
Bhuvaneshwar,
OD
Sri Vijaya Puram, Andaman and Nicobar Islands
Kochi,
KL
Flight Data Recorder
REST API
SevOne
Data Insight
vPAS NMS
vPAS NMS
vDNC
Poll (SNMP, SNMP TRAP, WMI, ICMP etc.)
NetFlow, sFlow, Netflow UDP 9996, etc.
Config / Performance
Config / Performance
Config / Performance
HAL Integrated Network Monitoring
Maximo® Application Suite
Network
devices
Hindustan Aeronautics Limited
Network
Peer to peer communication

## Slide 4
Hindustan Aeronautics Limited
Network
Customer Locations -
HAL Network
Porbandar,
GJ
Ratnagiri,
MH
Chennai,
TN
Bhuvaneshwar,
OD
Sri Vijaya Puram, Andaman and Nicobar Islands
Kochi,
KL
Flight Data Recorder
HAL User Authentication DataFlow
Https
Https
Https
Https
Https
Https
Secure Server Proxy
Sterling File Gateway
Secure File Gateway
Sterling External
Authentication Server
LDAP
1
2
3
4
5
6
7

## Slide 5
Hindustan Aeronautics Limited
Network
Customer Locations -
HAL Network
Porbandar,
GJ
Ratnagiri,
MH
Chennai,
TN
Bhuvaneshwar,
OD
Sri Vijaya Puram, Andaman and Nicobar Islands
Kochi,
KL
HAL FDR DataFlow
Sterling File Gateway
Control Center
Monitor / Director
Secure File Gateway
Red Hat OpenShift Cluster
Maximo® Application Suite
https(1)
https(1)
https(1)
https(1)
https(1)
https(1)
Maximo Monitor
IoT Tool
Asset Discovery
Internal Integration
DB2
Kafka
MongoDB
2
3
Reporting & Allied Software
4

## Slide 6
Physical Infrastructure Distribution
Machine | Site | Workload | Node Role | Servers | Nodes | vCPU | RAM (GB) | File Storage (GiB) | DB2 Storage (GiB) | GPU | OS | SOCKETS | Specifiction
M1 | Prod | MAS Prod | Master Nodes | Server 1 | 3 | 48 | 288 | 1560 | 0 | 0 | RHOCP | 2 | 2x Xeon Silver 4410Y, 12 Core, 512GB RAM, 2x 960GB SSD (RAID 1)
 |  |  | Worker Nodes | Server 2 | 21 | 336 | 996 | 4794 | 2495 | 3 |  | 2 | 2x Intel Xeon Gold 6444Y, 32 core, 512GB RAM, 2x 960GB SSD (RAID 1)
 |  |  |  | Server 3 |  |  |  |  |  |  |  | 2 | 
 |  |  |  | Server 4 |  |  |  |  |  |  |  | 2 | 
M2 | DR | MAS DR | Master Nodes | Server 5 | 3 | 48 | 288 | 1560 | 0 | 0 | RHOCP | 2 | 2x Xeon Silver 4410Y, 12 Core, 512GB RAM, 2x 960GB SSD (RAID 1)
 |  |  | Worker Nodes | Server 6 | 21 | 336 | 996 | 4794 | 2495 | 0 |  | 2 | 2x Intel Xeon Gold 6444Y, 32 core, 512GB RAM, 2x 960GB SSD (RAID 1)
 |  |  |  | Server 7 |  |  |  |  |  |  |  | 2 | 
 |  |  |  | Server 8 |  |  |  |  |  |  |  | 2 | 
M3 | UAT | MAS UAT | Master Nodes | Server 9 | 3 | 48 | 288 | 0 | 0 | 0 | RHOCP | 2 | 2x Xeon Silver 4410Y, 12 Core, 512GB RAM, 2x 960GB SSD (RAID 1)
 |  |  | Worker Nodes | Server 10 | 7 | 112 | 174 | 2459 | 768 | 1 |  | 2 | 2x Intel Xeon Gold 6444Y, 32 core, 512GB RAM, 2x 960GB SSD (RAID 1)
M4 | DMZ | SFG-SSP Prod | Application Nodes | Server 11 | N/A | 8 | 16 | 50 |  | N/A | RHEL | 2 | 1x Xeon Silver 6454S, 12 Core, 128GB RAM, 2x 960GB SSD (RAID 1)
M5 | Prod | SFG, Instana, SevOne | Application Nodes | Server 12 | N/A | 72 | 220 | 5874 | 1024 | N/A | RHEL | 2 | 1x Xeon Silver 6454S, 24 Core, 128GB RAM, 2x 960GB SSD (RAID 1)
 |  |  | Application Nodes | Server 13 | N/A |  |  |  |  |  | RHEL | 2 | 
M6 | DMZ | SFG-SSP UAT | Application Nodes | Server 14 | N/A | 8 | 16 | 50 |  | N/A | RHEL | 2 | 1x Xeon Silver 4410Y, 12 Core, 128GB RAM, 2x 960GB SSD (RAID 1)
M7 | UAT | SFG, Instana, SevOne | Application Nodes | Server 15 | N/A | 46 | 160 | 2650 | 250 | N/A | RHEL | 2 | 1x Xeon Silver 4410Y, 24 Core, 256GB RAM, 2x 960GB SSD (RAID 1)
M8 | Prod | Reporting & Allied Software | Application Nodes | Server 16 | N/A | 32 | 128 | 1028 | 2056 | N/A | Windows | 2 | 1x Xeon Silver 4410Y, 12 Core, 128GB RAM, 2x 960GB SSD (RAID 1)
 |  |  | Application Nodes | Server 17 | N/A |  |  |  |  |  | Windows | 2 | 
M9 | DR | Reporting & Allied Software | Application Nodes | Server 18 | N/A | 32 | 128 | 1028 | 2056 | N/A | Windows | 2 | 1x Xeon Silver 4410Y, 12 Core, 128GB RAM, 2x 960GB SSD (RAID 1)
 |  |  | Application Nodes | Server19 | N/A |  |  |  |  |  | Windows | 2 | 

## Slide 7
Physical Infrastructure Distribution
Site A DC
Site B DR

## Slide 8
Machine 1 (Production) MAS Cluster Environment | Machine 1 (Production) MAS Cluster Environment
384 VCPU | 1572 RAM(GB)
Machine 4 (Production) Standalone Environment for Instana ,SevOne,SFG | Machine 4 (Dev/UAT) Standalone Environment
72 VCPU | 220 RAM(GB)
Machine 3 (Dev/UAT) MAS Cluster Environment | Machine 1 (DR) MAS Cluster Environment
160 CPU | 750 RAM(GB)
DR SAN Total Storage | DR SAN Total Storage File Storage 288 GB
File Storage(GB) 7914 | DB Storage(GB) 2495
DC SAN Total Storage | Dev/ UAT SAN Total Storage | Dev/ UAT SAN Total Storage | 
MAS File Storage(GB) – 2459 DB Storage(GB) – 768 | SFG File Storage(GB) – 250 DB Storage(GB) – 250 | Instana File Storage(GB) – 76 DB Storage(GB) – 2000 | SevOne File Storage(GB) – DB Storage(GB) – 400
Machine 5 (Dev/UAT) Standalone Environment for Instana ,SevOne,SFG | Machine 5 (Dev/UAT)
42 VCPU | 140 RAM(GB)
Machine 6 ( Production Backup Software /Jump Server) | Machine 6 (Production) Standalone Environment
24 VCPU | 256 RAM(GB)
Machine 7 ( DR Backup Software /Jump Server) | Machine 7 (DR Backup Software Jump Server)
24 VCPU | 256 RAM(GB)
Physical Infrastructure Layout
Machine 2 (DR) MAS Cluster Environment | Machine 1 (DR) MAS Cluster Environment
384 VCPU | 1572 RAM
DC SETUP
DR SETUP

## Slide 9
Machine 2
PROD DC
Machine 1
Prod DR
Machine 3
UAT DR
SevOne
SFG
Instana
Machine 6
Prod Backup/Jump
Server
Machine 7
DR
Backup/Jump
Servers
MAS Cluster
Machine 4 & Machine 5
Standalone Environment
Backup/Jump Servers
MAS
Cluster
LOGICAL INFRASTRUCTURE LAYOUT

## Slide 10: Rack Elevation Plan - DC
RACK 1 | 
Space | Device
42 | 
41 | LIU
40 | 
39 | Cable Manager
38 | 
37 | Jack Pannel
36 | 
35 | Rack Switch
34 | 
33 | 
32 | KVM Switch
31 | 
30 | 
29 | 
28 | 
27 | 
26 | 
25 | 
24 | Maximo Prod 1
23 | 
22 | 
21 | Maximo Prod 2
20 | 
19 | 
18 | Maximo Prod 3
17 | 
16 | 
15 | Maximo Prod 4
14 | 
13 | 
12 | SevOne Prod
11 | 
10 | 
9 | SFG Prod
8 | 
7 | 
6 | Instana Prod
5 | 
4 | 
3 | Backup/SAN Server DC
2 | 
1 | 
RACK 2 | 
Space | Device
42 | 
41 | LIU
40 | 
39 | Cable Manager
38 | 
37 | Jack Pannel
36 | 
35 | Rack Switch
34 | 
33 | 
32 | KVM Switch
31 | 
30 | 
29 | 
28 | 
27 | 
26 | 
25 | 
24 | Maximo UAT 1
23 | 
22 | 
21 | Maximo UAT 2
20 | 
19 | 
18 | SevOne / Instana UAT
17 | 
16 | 
15 | SFG UAT
14 | 
13 | 
12 | Backup/SAN Server DC
11 | 
10 | 
9 | SAN - UAT
8 | 
7 | 
6 | Jump Server DC
5 | 
4 | 
3 | 
2 | 
1 | 

## Slide 11: Rack Elevation Plan - DC
RACK 3 | 
Space | Device
42 | 
41 | LIU
40 | 
39 | Cable Manager
38 | 
37 | Jack Pannel
36 | 
35 | Rack Switch
34 | 
33 | 
32 | PA-5410
31 | 
30 | 
29 | PA-5410
28 | 
27 | 
26 | FG-400F
25 | 
24 | 
23 | FG-400F
22 | 
21 | 
20 | LLB
19 | 
18 | 
17 | LLB
16 | 
15 | 
14 | SLB
13 | 
12 | 
11 | SLB
10 | 
9 | 
8 | WAF
7 | 
6 | 
5 | WAF
4 | 
3 | 
2 | 
1 | 
RACK 4 | 
Space | Device
42 | 
41 | LIU
40 | 
39 | Cable Manager
38 | 
37 | Jack Pannel
36 | 
35 | ISR 4461
34 | 
33 | 
32 | ISR 4461
31 | 
30 | 
29 | ISR 4461
28 | 
27 | 
26 | ISR 4461
25 | 
24 | 
23 | N9K-C9316D-GX
22 | 
21 | 
20 | N9K-C9316D-GX
19 | 
18 | 
17 | N9K-C93180YC-EX
16 | 
15 | 
14 | N9K-C93180YC-EX
13 | 
12 | 
11 | N9K-C93180YC-EX
10 | 
9 | 
8 | N9K-C93180YC-EX
7 | 
6 | 
5 | N9K-C93180YC-EX
4 | 
3 | 
2 | N9K-C93180YC-EX
1 | 

## Slide 12: Rack Elevation Plan - DR
RACK 1 | 
Space | Device
42 | 
41 | LIU
40 | 
39 | Cable Manager
38 | 
37 | Jack Pannel
36 | 
35 | Rack Switch
34 | 
33 | 
32 | KVM Switch
31 | 
30 | 
29 | 
28 | 
27 | 
26 | 
25 | 
24 | Maximo DR 1
23 | 
22 | 
21 | Maximo DR 2
20 | 
19 | 
18 | Maximo DR 3
17 | 
16 | 
15 | Maximo DR 4
14 | 
13 | 
12 | 
11 | 
10 | 
9 | 
8 | 
7 | 
6 | Jump Server DR
5 | 
4 | 
3 | Backup/SAN Server DC
2 | 
1 | 
RACK 2 | 
Space | Device
42 | 
41 | LIU
40 | 
39 | Cable Manager
38 | 
37 | Jack Pannel
36 | 
35 | Rack Switch
34 | 
33 | 
32 | PA-5410
31 | 
30 | 
29 | PA-5410
28 | 
27 | 
26 | FG-400F
25 | 
24 | 
23 | FG-400F
22 | 
21 | 
20 | LLB
19 | 
18 | 
17 | LLB
16 | 
15 | 
14 | SLB
13 | 
12 | 
11 | SLB
10 | 
9 | 
8 | WAF
7 | 
6 | 
5 | WAF
4 | 
3 | 
2 | 
1 | 
RACK 3 | 
Space | Device
42 | 
41 | LIU
40 | 
39 | Cable Manager
38 | 
37 | Jack Pannel
36 | 
35 | ISR 4461
34 | 
33 | 
32 | ISR 4461
31 | 
30 | 
29 | ISR 4461
28 | 
27 | 
26 | ISR 4461
25 | 
24 | 
23 | N9K-C9316D-GX
22 | 
21 | 
20 | N9K-C9316D-GX
19 | 
18 | 
17 | N9K-C93180YC-EX
16 | 
15 | 
14 | N9K-C93180YC-EX
13 | 
12 | 
11 | N9K-C93180YC-EX
10 | 
9 | 
8 | N9K-C93180YC-EX
7 | 
6 | 
5 | N9K-C93180YC-EX
4 | 
3 | 
2 | N9K-C93180YC-EX
1 | 

## Slide 13
WEB/App Zone
Dmz leaf switch
Perimeter Firewall
IPS
LLB
Border leaf Switch
LLB
Internet Router
MPLS Router
SLB
DMZ HOST
MGMT
MZ/DB Zone
Compute
Storage
FI
Spine Switch
service leaf switch
Core Firewall
Compute leaf switch
WAF
HAL Integrated Asset Management and Monitoring Platform network HLD for DC
10 Gig Fiber
100 Gig Fiber
1 Gig Fiber
25 Gig Fiber
16 Gig FC
Switch to Switch Connectivity
Compute to Leaf Switch Connectivity
Storage to Leaf Switch Connectivity
Active Network component connectivity
Internet connectivity with Border Leaf Switch

## Slide 14
MZ VM
UCS series server
WEB/App Zone
Dmz leaf switch
Perimeter Firewall
IPS
LLB
Border leaf Switch
LLB
Internet Router
MPLS Router
SLB
DMZ HOST
MGMT
MZ/DB Zone
Storage
FI
Spine Switch
service leaf switch
Core Firewall
Compute leaf switch
WAF
HAL Integrated Asset Management and Monitoring Platform network HLD for DR
10 Gig Fiber
100 Gig Fiber
1 Gig Fiber
25 Gig Fiber
16 Gig FC
Switch to Switch Connectivity
Compute to Leaf Switch Connectivity
Storage to Leaf Switch Connectivity
Active Network component connectivity
Internet connectivity with Border Leaf Switch
Compute

## Slide 15: V-Lan Segment Distribution
Specifications | Segment
Network MGMT | 101
Compute MGMT | 102
DMZ | 103
MZ | 104
DB | 105
Security MGMT | 106
Internet Link | 107,108
MPLS Link | 109,110
Common Service | 111

## Slide 16: THANK YOU…..